## Slide 1
Chapter11 DSP Algorithm Implementation
Structure Simulation and Verification by MATLAB
Computation of DFT
Fast Fourier Transformation —— FFT
  DIT
  DIF
11.2.1, 11.2.2, 11.2.3, 11.2.4, 11.3.2, 11.3.3, 11.3.4, 11.5

## Slide 2: 11.2 Structure simulation Using MATLAB
Program:
direct2.m, 11_1.m, 11_2.m, 11_3.m, 11_4.m, 11_5.m, 11_6.m
11.3 Computation of the DFT
11.3.1 Goertzel’s Algorithm（了解）
11.5 DFT and IDFT Computation Using MATLAB
Program 11_10.m --Spectral Analysis
Program 11_11.m --Linear Convolution

## Slide 3
FFT--Fast Fourier Transformation, not a new transformation, but a fast algorithm to calculate the DFT.
J.W.Cooley and J.W.Tukey are given credit for bringing the FFT to the world in their paper :“An algorithm for the machine calculation of complex Fourier Series”, Mathematics Computation, Vol.19, 1965.
IEEE电声汇刊在1967年出版快速傅里叶变换算法专辑开始了快速变换的历史。
IEEE signal processing Magazine 1992年1月和IEEE ICASSP 92都有特约文章或报告纪念FFT专辑的发表。
1994年4月出版了《理解傅里叶技术》的专辑，目的在于普及和推广FFT技术。
11.3.2 Cooley-Tukey FFT Algorithms
Notes: Mooc补充材料

## Slide 4
传统快速傅里叶变换算法是递归分解算法，包含基2、基4、基8 和分裂基FFT。
Stasinisik 提出的基K-FFT (又称卷积FFT 算法c-FFT)是其它基数FFT算法的新发展。
Frigo and Johnson于2005年开发了FFTW的免费库，提供将FFT算法在多种硬件平台上运行的解决方案。
当N为复合数，即N可以分解为k和m的积时，可以通过二维序号映射实现快速算法，称为素因子FFT算法。
Notes: 11.4节有进一步的介绍

## Slide 5
DFT and IDFT definition:
Where,
Direct computation of all N samples of {X[k]} requires N2 complex multiplications and N(N-1) complex additions.
Notes: We can see that the same values of WN are calculated many times during the DFT,
since WN is a periodic function with a limited number of distinct values.
The aim of the FFT and its inverse, the IFFT, is to use this redundancy to reduce the number of calculation.

## Slide 6
The properties of twiddle factor WN
Periodicity:
Reduction:
Symmetry:

## Slide 7: Decimation-in-Time FFT
Given a sequence x[n] whose length is N=2k, k is an integer.
Divided the sequence into even index sequences and odd index sequences:
Since x[n] is first decimated to form a set of subsequences before the DFT is computed, this computation schemes are called decimation-in-time (DIT) FFT algorithms.

## Slide 8: Decimation-in-Time FFT
We get:
Where X0[k] and X1[k] is N/2-point DFT, so we get only first half N/2-point result of X[k].

## Slide 9: Decimation-in-Time FFT
Based on the periodicity of WN, we can get:
And:
So:

## Slide 10
Block-diagram interpretation:
2
x[n]
x0[n]=x[2n]
2
x[n]
x1[n]=x[2n+1]
z
x[n+1]
N/2-point
DFT
N/2-point
DFT
2
2
z

## Slide 11: Decimation-in-Time FFT
The computation of N-point DFT by two methods:
DFT computation | Complex Addition | Complex Multiplication
Direct computation | N2-NN2 | N2
DIT to two N/2-point DFT | (N2/2)+N | (N2/2)+N

## Slide 12: Decimation-in-Time FFT
继续将 x0[n] and x1[n] 分解成 2个 (N/4)-point DFTs
where X00[k] and X01[k] are the (N/4)-point DFTs of the (N/4)-length sequences: x00[n]= x0[2n] and x01[n]= x0[2n+1]
where X10[k] and X11[k] are the (N/4)-point DFTs of the (N/4)-length sequences： x10[n] = x1[2n] and x11[n] = x1[2n+1]

## Slide 13: Decimation-in-Time FFT
The following figure shows the time domain decomposition used in the FFT:
1 signal of 8 points
2 signal of 4 points
4 signals of 2 points
0 1 2 3 4 5 6 7
0 2 4 6
1 3 5 7
0 4
2 6
1 5
3 7

## Slide 14: Decimation-in-Time FFT
Flow-graph representation
Notes: In the flow-graph shown N =8；
Hence, the (N/4)-point DFT here is a 2-point DFT and no further decomposition is possible.
The four 2-point DFTs, Xij[k], i, j=0, 1 can be easily computed.

## Slide 15
Complete flow-graph of the 8-point DFT is shown below
Each stage of the DFT computation process employs the same basic computational module which is called a butterfly computation.
Notes: The flow-graph consists of 3 stages:
  First stage computes the four 2-point DFTs
  Second stage computes the two 4-point DFTs
  Last stage computes the desired 8-point DFT

## Slide 16: Decimation-in-Time FFT
Total number of complex multiplications and additions to compute all 8 DFT samples is equal to 8 + 8 + 8 = 24 = 83.
In the general case when N=2k , number of stages for the computation of the (2k )-point DFT in the fast algorithm will be k=log2N.
Total number of complex multiplications to compute all N DFT samples is N( log2N)/2
Total number of complex additions to compute all N DFT samples is N( log2N)
如果考虑 and ，以及 ，运算量还会减少。

## Slide 17: Decimation-in-Time FFT
Notes: The fast algorithm described assumes that the length of x[n] is a power of 2;
If it is not, the length can be extended by zero-padding and make the length a power of 2;
the smallest DFTs are 2-point DFTsradix-2

## Slide 18: Decimation-in-Time FFT
FFT利用同址计算（in-place computation）可以降低总的存储需求；
  每级计算的输出可以占用上级输入相同的寄存器
前面蝶形运算中，输入和输出序号不一致；可利用硬件位倒序（bit-reversed order）寻址实现。
Notes: At the end of computation at any stage, output variables can be stored in the same registers previously occupied by the corresponding input variables;
This type of memory location sharing is called in-place computation resulting in significant savings in overall memory requirements.
In the DFT computation scheme outlined, the DFT samples X[k] appear at the output in a sequential order while the input samples x[n] appear in a different order;
Thus, a sequentially ordered input x[n] must be reordered appropriately before the fast algorithm described by this structure can be implemented.

## Slide 19
original original bit-reversed bit-reversed
order address address order
0 000 000 0
1 001 100 4
2 010 010 2
3 011 110 6
4 100 001 1
5 101 101 5
6 110 011 3
7 111 111 7
Notes: if n=( b2b1b0 ) represents the index of x[n], then m=( b0b1b2 ) is the correct index for FFT input samples.

## Slide 20: Decimation-in-frequency FFT
Given a sequence x[n] whose length is N=2L, L is an integer. And dividing the sequence into two half sequences and compute its DFT:

## Slide 21: Decimation-in-frequency FFT
When k is even number:
When k is odd number:
Because , and , then:

## Slide 22: Decimation-in-frequency FFT
Based on , above formula equals to:
Process is continued until the smallest DFTs are 2-point DFTs.

## Slide 23: Decimation-in-frequency FFT
Complete flow-graph of the DIF FFT computation scheme for N = 8.

## Slide 24: Decimation-in-frequency FFT
Computational complexity of the radix-2 DIF FFT algorithm is same as that of the DIT FFT algorithm.
Various forms of DIF FFT algorithm can similarly be developed.
It can be easily seen that the flow-graph of DIF FFT is the transpose of the flow-graph of DIT FFT, and vice-versa.

## Slide 25: Inverse DFT Computation
An FFT algorithm for computing the DFT samples can also be used to calculate the inverse DFT (IDFT) efficiently.
Consider a length-N sequence x[n] with an N-point DFT X[k]:

## Slide 26: Inverse DFT Computation
Right-hand side of above is the N-point DFT of X*[k].
Desired IDFT x[n] is then obtained as:

## Slide 27: Inverse DFT Computation
Inverse DFT computation is shown below:
Re{X[k]}
Re{x[n]}
Im{x[n]}
Im{X[k]}
N-point
DFT

## Slide 28: Homework:
11.17，11.18
M11.2, M11.3