## Slide 1
§2 Discrete-Time Signals In the Time-Domain
The time-domain representation of discrete-time signals
Operations on sequences
Classification of Sequences
Typical sequences
The Sampling Process
Outline

## Slide 2
Discrete-time signal may also be written as a sequence of numbers inside braces:
{x[n]}={…, -0.2, 2.2, 1.1, 0.2, -3.7, 2.9,…}

n = 0
In the above, x[-1]= -0.2, x[0]=2.2, x[1]=1.1, etc.
§2 Discrete-Time Signals In the Time-Domain
values of argument n defined only for integer and undefined for noninteger values of n
2.1 Time-Domain Representation

## Slide 3
Graphical representation of a discrete-time signal with real-valued samples is as shown below:
§2 Discrete-Time Signals In the Time-Domain

## Slide 4
In some applications, a discrete-time sequence {x[n]} may be generated by periodically sampling a continuous-time signal xa(t) at uniform intervals T of time
§2 Discrete-Time Signals In the Time-Domain
Whether or not the sequence {x[n]} has been obtained by sampling, the quantity x[n] is called the n-th sample of the sequence

## Slide 5
Here, n-th sample is given by
x[n]=xa(t) |t=nT=xa(nT), n=…,-2,-1,0,1,…
The spacing T between two consecutive samples is called the sampling interval or sampling period
Reciprocal of sampling interval T, denoted as FT , is called the sampling frequency:
FT=1/T
Unit of sampling frequency is cycles per second, or hertz (Hz), if T is in seconds
§2 Discrete-Time Signals In the Time-Domain
MOOC

## Slide 6
Two types of discrete-time signals:
  - Sampled-data signals in which samples are continuous-valued
  - Digital signals in which samples are discrete-valued
Signals in a practical digital signal processing system are digital signals obtained by quantizing the sample values either by rounding or truncation
§2 Discrete-Time Signals In the Time-Domain

## Slide 7
{x[n]} is a real sequence, if the n-th sample x[n] is real for all values of n; Otherwise, {x[n]} is a complex sequence
A complex sequence {x[n]} can be written as
{x[n]}={xre[n]} + j{xim[n]}
where xre[n] and xim[n] are the real and imaginary parts of x[n]
The complex conjugate sequence of {x[n]} is given by
{x*[n]}={xre[n]} - j{xim [n]}
§2 Discrete-Time Signals In the Time-Domain

## Slide 8
Example - {x[n]}={cos0.25n} is a real sequence
{y[n]}={ej0.3n} is a complex sequence
We can write
{y[n]}={cos0.3n + jsin0.3n}
= {cos0.3n} + j{sin0.3n}
where {yre[n]}={cos0.3n}
{yim[n]}={sin0.3n}
{y*[n]}={cos0.3n} - j{sin0.3n}
§2 Discrete-Time Signals In the Time-Domain

## Slide 9
A discrete-time signal may be a finite-length or an infinite-length sequence
Finite-length (also called finite-duration or finite-extent) sequence is defined only for a finite time interval:
N1 n  N2
where - < N1 and N2 <  with N1 N2
Length or duration of the above finite-length sequence is N= N2 - N1+ 1
Zero-padding—append with zero-valued samples.
2.1.1 Length of a discrete-time signal
Vector form
x[n]=[x[0] x[1] … x[N-1]]
t
§2 Discrete-Time Signals In the Time-Domain

## Slide 10
A right-sided sequence x[n] has zero-valued samples for n < N1
A right-sided sequence
If N1 0, a right-sided sequence is called a causal sequence.
§2 Discrete-Time Signals In the Time-Domain

## Slide 11
A left-sided sequence x[n] has zero-valued samples for n > N2
If N2≤ 0, a left-sided sequence is called a anticausal sequence.
§2 Discrete-Time Signals In the Time-Domain
A left-sided sequence

## Slide 12
2.1.2 Strength of a Discrete-Time Signal
p is a positive integer.
In practice, the value of p used is typically 1 or 2 or
The strength of a DT Signal usually is given by its norm.
of {x[n]} is defied by
§2 Discrete-Time Signals In the Time-Domain

## Slide 13
Peak absolute value
For a length-N seqence,
is the root-mean-squared(rms) value of {x[n]}, and
is the mean absolute value of {x[n]}.
It can be shown that
norm(x,1)
norm(x,2)
norm(x,inf)
M-file in MATLAB
§2 Discrete-Time Signals In the Time-Domain

## Slide 14
For example, a length-N seqence y[n], and x[n],
One application of the norm is in estimating the error in approximation of a DT signal by another DT signal
0 n N-1
mean-squared error(MSE)
relative error
§2 Discrete-Time Signals In the Time-Domain

## Slide 15
2.2.1 Elementary Operations
MOOC
time-reversal (folding operation)
x[-n]
§2 Discrete-Time Signals In the Time-Domain

## Slide 18
Example 2.1 Ensemble average
original uncorrupted data
Noise
§2 Discrete-Time Signals In the Time-Domain

## Slide 19
Ensemble average
Vector form
S = [s[0] s[1] … s[N-1]]
t
The i-th measurement of data vector

## Slide 20
2.2.2 Combination of Elementary Operations
§2 Discrete-Time Signals In the Time-Domain

## Slide 21
Example
y[n]=1x[n]+ 2x[n-1]+ 3[n-2]+ 4x[n-3]
If 1=2=3=4=1/4, y[n]=1/4{x[n]+ x[n-1]+ [n-2]+x[n-3]

## Slide 22
M-point moving-average system
Ex：x[n] = s[n] + d[n]
s[n] = 2[n(0.9)n ], d[n] - random signal

## Slide 23: 2.2.3 Convolution Sum
y[n] = x[n] h[n]
*
is called the convolution sum of the sequences x[n] and h[n] and represented compactly as
MOOC
if the lengths of the two sequences being convolved are M and N, then the sequence generated by the convolution is of length M+N-1
§2 Discrete-Time Signals In the Time-Domain

## Slide 24: Convolution Sum Properties
Commutative property:
x[n] h[n] = h[n] x[n]
*
*
(x[n] h[n]) y[n] = x[n] (h[n] y[n])
*
*
*
*
x[n] (h[n] + y[n]) = x[n] h[n] + x[n] y[n]
*
*
*
Distributive property :
Associative property :
§2 Discrete-Time Signals In the Time-Domain

## Slide 25
Example Develop the sequence y[n] generated by the convolution of the sequences x[n] and h[n] :
x[n] = h[n] = δ[n] + δ[n-1] + δ[n-2]
*
MOOC
y[n]=δ[n]+2δ[n-1]+3δ[n-2]+2δ[n-3]+δ[n-4]
y[n ]
n
1
1
0
2
3
4
2
2
3
1
§2 Discrete-Time Signals In the Time-Domain

## Slide 26
x[k]
h[-k]
x[k]
h[1-k]
x[k]
h[2-k]
x[k]
x[k]
x[n] = h[n] = δ[n] + δ[n-1] + δ[n-2]
∑X[k]h[-k]
=1
X[k]h[-k]
k
k
X[k]h[1-k]
∑X[k]h[1-k]
=2
k
X[k]h[2-k]
k
X[k]h[3-k]
k
X[k]h[4-k]
h[4-k]
h[3-k]
∑X[k]h[2-k]
=3
∑X[k]h[3-k]
=2
∑X[k]h[4-k]
=1
x[k]
h[k]
1
1
MOOC
§2 Discrete-Time Signals In the Time-Domain

## Slide 27: Tabular Method of Convolution Sum Computation
Example: We want to obtain the convolution sum y[n] by the following steps:
n: 0 1 2 3 4 5
g[n]: g[0] g[1] g[2] g[3]
h[n]: h[0] h[1] h[2]
g[0]h[0] g[1]h[0] g[2]h[0] g[3]h[0]
g[0]h[1] g[1]h[1] g[2]h[1] g[3]h[1]
g[0]h[2] g[1]h[2] g[2]h[2] g[3]h[2]
y[n]: y[0] y[1] y[2] y[3] y[4] y[5]

## Slide 28
Example: x[n]=(1/2)n-2μ[n-2]
h[n]= μ[n+2]

## Slide 29: 2.2.4 Sampling rate alteration
Up-sampling
Down-sampling
MOOC
§2 Discrete-Time Signals In the Time-Domain

## Slide 30
Up-sampling (L=3)
MOOC
§2 Discrete-Time Signals In the Time-Domain

## Slide 31
Down-sampling (M=3)
MOOC
§2 Discrete-Time Signals In the Time-Domain