## Slide 1
§2 Discrete-Time Signals In the Time-Domain
The time-domain representation of discrete-time signals
Operations on sequences
Classification of Sequences
Typical sequences
The Sampling Process
Outline

## Slide 2
§ 2.3 Operations on Finite-length Sequences
MOOC
§2 Discrete-Time Signals In the Time-Domain
前面定义的运算对有限长序列不适用：
A length-N sequences x[n], 0≤n≤N-1; its sample values are equal to zero for values of n < 0 and n ≥ N.
x[– n] is defined for the range –(N-1) ≤n≤ 0.
for any arbitrary integer n0 , x1[n] = x[n – n0]
is no longer defined for the range 0≤n≤N-1.
必须定义有限长序列的运算，使得结果仍满足：
0 ≤ n ≤ N-1

## Slide 3
1. Classification based on Symmetry
Conjugate-symmetry sequence
x*[n] = x[-n]
Conjugate-antisymmetry sequence
x*[n] = -x[-n]
complex sequence x[n]
Even
y[n]=y[-n]
Odd
y[n]=-y[-n]
real y[n]
2.3.3 Classification of Sequences
Conjugate-symmetry part
Conjugate-antisymmetry part

## Slide 4
{g﹡[n]}={0, 1-j4, -2-j3, 4+j2, -5+j6, j2, 3}

{g﹡[-n]}={3, j2, -5+j6, 4+j2, -2-j3, 1-j4, 0}

§2 Discrete-Time Signals and Systems
{g[n]} = {0, 1+j4, -2+j3, 4-j2, -5-j6, -j2, 3}

Example 2.8 A length-7 sequence(n:[-3,3]):
{gcs [n]}={1.5,0.5+j3,-3.5+j4.5,4,-3.5-j4.5,0.5-j3,1.5}

{gca [n]}={-1.5,0.5+j,1.5-j1.5, -j2,-1.5-j1.5,-0.5+j,1.5}


## Slide 5: 2.Classification of Sequences based on periodicity
Example
§2 Discrete-Time Signals and Systems
A sequence satisfying the periodicity condition
is called an periodic sequence
for all n
MOOC

## Slide 6
Adding two periodic sequences with different fundamental periods
§2 Discrete-Time Signals and Systems
The fundamental period：
GCD( )---greatest common divider
LCM( )---least common multiple
fundamental periods
MOOC

## Slide 7
Example
Its fundamental period is 48,
because the GCD of 16 and 12 is 4.
§2 Discrete-Time Signals and Systems
MOOC
=
=

## Slide 8: 3. Energy and Power Signals
Total energy of a sequence x[n] is defined by
§2 Discrete-Time Signals and Systems
The average power of a sequence is defined by

## Slide 9
Example - Power signal:
Note: x[n] has infinite energy
Its average power is given by
§2 Discrete-Time Signals and Systems
Power signal: an infinite energy signal with finite average power.

## Slide 10
Example - Energy signal:
Energy signal: a finite energy signal with zero average power.
§2 Discrete-Time Signals In the Time-Domain

## Slide 11: 4. Other Types of Classification
A sequence x[n] is said to be bounded if
Example - The sequence x[n]=cos(0.3n) is a bounded sequence as
§2 Discrete-Time Signals In the Time-Domain

## Slide 12
A sequence x[n] is said to be absolutely summable if
Example - The sequence
is an absolutely summable sequence as
§2 Discrete-Time Signals In the Time-Domain

## Slide 13
A sequence x[n] is said to be square-summable if
Example - The sequence
is square-summable but not absolutely summable
§2 Discrete-Time Signals In the Time-Domain

## Slide 14
It is neither absolutely summable nor square-summable .
Example - The sequence obtained by adding an absolutely summable sequence with its replicas shifted by integer multiples of N,
is called an N-periodic extension of .
§2 Discrete-Time Signals In the Time-Domain

## Slide 15
Unit sample sequence
Unit step sequence
§ 2.4 Typical Sequences and Representation
2.4.1 Basic Sequences
MOOC

## Slide 16: 2.4.3 Representation of an Arbitrary Sequence by impulses
An arbitrary sequence can be represented in the time-domain as a weighted sum of some basic sequence and its delayed (advanced) versions
MOOC
§2 Discrete-Time Signals In the Time-Domain

## Slide 17
Example
§2 Discrete-Time Signals In the Time-Domain

## Slide 18
Rectangular Window Sequence
Box-car sequence
Windowing
§2 Discrete-Time Signals In the Time-Domain

## Slide 19
Sinusoidal Sequence
where A is the amplitude, 0 is the normalized angular frequency, and  is the phase of x[n].
The unit of 0 and  is radians/sample
Often in practice, 0 is expressed as 0=2f0
Where f0 is normalized frequency in cycles/sample
§2 Discrete-Time Signals In the Time-Domain

## Slide 20
Sinusoidal Sequence
  We can write as
  is the in-phase components of x[n] and
  is the quadrature components of x[n].
§2 Discrete-Time Signals In the Time-Domain

## Slide 21
when A and are real or complex numbers.
Exponential Sequence
MOOC
The Complex Exponential Sequence

## Slide 22
The complex sinusoidal sequence
Exponential Sequence

## Slide 23
when A and are real numbers, it’s a real exponential sequence.
Real Exponential Sequence
MOOC
§2 Discrete-Time Signals In the Time-Domain

## Slide 24: 2.4.2 Sequence Generation Using MATLAB
n=0:40;
K=1;
c=(-1+j*2*pi)/12;
x=K*exp(c*n);
stem(n, real(x));
title('Real part');
stem(n, imag(x));
title('Imaginary part');

## Slide 25
If 2/0 is an rational number,
the sequence x[n]=Acos(0n+) is periodic.
Otherwise, it’s aperiodic.
* The periodicity of sinusoidal and exponential sequence *
MOOC
How to determine the fundamental period?
Why?
§2 Discrete-Time Signals In the Time-Domain

## Slide 26
Only if sin0N= 0 and cos0N = 1,
Smallest value of N satisfying 0N=2r
is the fundamental period of the sequence.
MOOC
These two conditions are met if and only if
0N = 2r
or 2 / 0 = N/r
where N and r are positive integers.
To verify the periodicity condition, consider
=A cos 0N - sin(0n + )sin0N

## Slide 27
Example - x[n]=sin(3n) is an aperiodic sequence.
y[n]=cos(0.1n) is a periodic sequence.
0 = 0.1
N= 2r/0
= 20 for r = 1
MOOC
§2 Discrete-Time Signals In the Time-Domain

## Slide 28
N= 2r/0
= 20, r=1
N= 2r/0
= 5, r=2
N= 2r/0
= 10, r=1
N= 2r/0
= 2, r=1
§2 Discrete-Time Signals In the Time-Domain

## Slide 29
Two Properties of Sinusoidal Sequence
1. Consider: x1[n]=Acos(1n+), x2[n]= Acos(2n+)
Where, 0≤ 1<2π, and 2πk ≤ 2<2π(k+1)
k is an any positive integer.
Then x2[n] = Acos((1+2πk) n+) = x1[n]
If
2 = 1+2πk
(indistinguishable)
MOOC
2 is equivalent to 1modulo 2π

## Slide 30
2.The highest  of Sinusoidal Sequence is .
folding frequency
Two Properties of Sinusoidal Sequence

## Slide 31
Often, a discrete-time sequence x[n] is developed by uniformly sampling a continuous-time signal xa(t) as indicated below
x[n]=xa(t)|t=nT=xa(nT), n=…, -2, -1, 0, 1, 2, …
§ 2.5 The Sampling Process
§2 Discrete-Time Signals In the Time-Domain

## Slide 32
Time variable t of xa(t) is related to the time variable n of x[n] only at discrete-time instants tn given by
MOOC
Here:
---sampling frequency
---sampling angular frequency
§2 Discrete-Time Signals In the Time-Domain

## Slide 33
Sampling a continuous-time Sinusoidal signal
is the normalized digital angular frequency of x[n]
where
The corresponding discrete-time signal is
MOOC
The unit of 0 is radians/sample
§2 Discrete-Time Signals In the Time-Domain

## Slide 34
Note: The Ambiguity in the DT Representation of CT Signals
Example:
Three continuous-time signals
of frequencies 3 Hz, 7 Hz, and 13 Hz,
MOOC
While sample distance T=0.1sec, the derived sequences are:
§2 Discrete-Time Signals In the Time-Domain

## Slide 35
Plots of these sequences (shown with circles) and their parent time functions:
Note that each sequence has exactly the same sample value for any given n
0
0.2
0.4
0.6
0.8
1
-1
-0.5
0
0.5
1
time
Amplitude
MOOC
§2 Discrete-Time Signals In the Time-Domain

## Slide 36
This fact can also be verified by observing that
As a result, all three sequences are identical and it is difficult to associate a unique continuous-time function.
Why?
§2 Discrete-Time Signals In the Time-Domain

## Slide 37
The above phenomenon of a continuous-time signal of higher frequency acquiring the identity of a sinusoidal sequence of lower frequency after sampling is called aliasing.
Recall: 0 = 20 / T
Thus if T > 20, then 0 of the discrete-time signal obtained by sampling the parent continuous-time sinusoidal signal will be in the range -<<.
No aliasing
§2 Discrete-Time Signals In the Time-Domain
If T < 20 , the 0 will fold over into a lower digital frequency in the range
-<< because of aliasing.
Hence, to prevent aliasing, the sampling theorem requires T > 20

## Slide 38: Homework
2.3, 2.4(a) (b), 2.5, 2.9, 2.19, 2.21, 2.27, 2.28, 2.35(a)(b), 2.39, 2.47, 2.51;
M2.3, M2.4