## Slide 1
Chapter 9 IIR Digital Filter Design
Preliminary Considerations
IIR Digital Filter Design Methods
MATLAB Functions in IIR Filter Design

## Slide 2
Objective：
Determination of a realizable transfer function G(z) approximating a given frequency response specification is an important step in the development of a digital filter.
If an IIR filter is desired, G(z) should be a stable real rational function.
Digital filter design is the process of deriving the transfer function G(z).
Filter Design Objective

## Slide 3
These are two issues that need to be considered before one can develop the digital transfer function G(z).
  The first and foremost issue is the development of a reasonable filter frequency response specification.
  Usually, either the magnitude and/or the phase response is specified for the design of digital filter for most applications;
  We restrict to the magnitude approximation problem in this chapter.
  The second issue is to determine whether an FIR or an IIR digital filter is to be designed.
9.1 Preliminary Considerations
Notes: In most practical applications, the problem of interest is the development of a realizable approximation to a given magnitude response specification.

## Slide 4
Digital Filter Design Specifications
The magnitude response |G(ej)| of a digital lowpass filter may be specified below:
In the passband, we require
1- p  |G(ej)|  1+ p,
p : passband edge freq.
s: stopband edge freq.
p : passband peak ripple
s : stopband peak ripple
In the stopband, we require | G(ej)|  s

## Slide 5
Digital Filter Design Specifications

## Slide 6
9.1.1 Digital Filter Specifications
通带最大幅度设为1(unity)
Maximum passband deviation
Maximum stopband magnitude
1/A = s
Maximum passband attenuation
For p<<1
Magnitude specifications may be given in a normalized form as indicated below:

## Slide 7
Digital Filter Design Specifications
In practice, passband edge frequency fp and stopband edge frequency fs are specified in Hz.
where Fs and Ts are sampling frequency and sampling interval
For digital filter design, normalized angular edge frequencies can be computed in radians as
Mooc 内容

## Slide 8
Example 9.1
Let p=0.1dB, and s= 35dB. Determine the p and s
9.1.1 Digital Filter Specifications

## Slide 9
Example 9.2
Let Fp= 7 kHz, Fs= 3 kHz, and FT=25 kHz
Then
9.1.1 Digital Filter Specifications

## Slide 10
The objective of digital filter design is to develop a casual, stable transfer function G(z) which meets the FR specifications.
Whether IIR or FIR should be selected?
9.1.2 Selection of the Filter Type
IIR: lower order to reduce computational complexity; but must be stable.
FIR: linear phase; always stable; but higher order.

## Slide 11
Most common approach to IIR filter design:
Transform it into the desired digital filter transfer function G(z).
Convert the digital filter specifications into analog lowpass prototype one.
Determine the analog lowpass filter Ha(s) meeting these specifications.
9.1.3 Basic Approach to IIR Digital Filter Design

## Slide 12
Why this approach has been widely used:
(1) Analog approximation techniques are highly advanced.
(2) They usually yield closed-form solutions.
(3) Extensive tables are available for analog filter design.
(4) Many applications require digital simulation of analog systems.
9.1.3 Basic Approach to IIR Digital Filter Design

## Slide 13
The basic idea is to apply a mapping from s-domain to the z-domain so that the essential properties of the analog frequency response are preserved. [Ha(s) --＞ G(z)]
This implies that the mapping should be:
(1) The imaginary axis in the s-plane be mapped onto the unit circle of the z-plane.
(2) A stable analog transfer function be transformed into a stable digital transfer function.
9.1.3 Basic Approach to IIR Digital Filter Design

## Slide 14
After the type of the digital filter has been selected, the next step in the filter design process is to estimate the filter order N.
For the design of IIR LPF, the order of Ha(s) is estimated from its specifications using the appropriate formula given in Eq.(A.9), (A.17), or (A.27), depending on which approximation is desired.
Then the order of G(z) can be determined automatically from the transformation being used to convert Ha(s) into G(z).
9.1.4 IIR Digital Filter Order Estimation

## Slide 15
In magnitude scaling, the transfer function G(z) is multiplied by a constant K so that the maximum magnitude of the KG(z) in the passband is unity; it has a maximum gain of 0dB.
If Gmax is the maximum value of |G(ejw)| in the passband, then K=1/ Gmax
  For a lowpass G(z) with a maximum magnitude at DC, K=1/G(1);
  For a highpass G(z) with a maximum magnitude at w=p, K=1/G(-1);
  For a bandpass G(z), K=1/Gejwc, where wc is the center frequency of the passband.
9.1.5 Scaling the Digital Transfer function

## Slide 16
Analog Filter Specifications
Butterworth approximation
Chebyshev approximation
Type1 Type2
Elliptic approximation
Analog Lowpass Filter Design Using MATLAB
Appendix A: Analog Filter Design

## Slide 17
p -passband edge frequency
s -stopband edge frequency
p -peak ripple value in the passband
s -peak ripple value in the stopband
Analog Lowpass Filter Specifications

## Slide 18
Transtion ratio or selectivity parameter:
Discrimination parameter:
Normalized magnitude specifications for an analog lowpass filter

## Slide 19
In the passband, defined by 0   p
1-p  |Ha(j)|  1+ p , ||  p
In the stopband, defined by s    ,
|Ha(j)|  s , s    
Peak passband ripple
Minimum stopband attenuation
Notes: |Ha(j)| approximates unity within an error of p ;
|Ha(j)| approximates zero within an error of s

## Slide 20
Attenuation function or Loss function

## Slide 21
Transition ratio or Selectivity parameter

## Slide 22
Butterworth Approximation
The magnitude-square response of an N-th order analog lowpass Butterworth filter is given by:
The Butterworth lowpass filter thus is said to have a maximally-flat magnitude at  = 0.
Appendix A: Analog Filter Design
Two parameters completely characterizing a Butterworth lowpass filter are c and N.

## Slide 23
Gain in dB is: G()=10log10|Ha(j)|2
As G(0)=0 and
G(c)=10log10(0.5) -3 dB
c is called 3-dB cutoff frequency.
Typical magnitude responses with c =1 are shown in right.
Butterworth Approximation

## Slide 24
Ωc and N are determined from:
Solving the above, we get:
Butterworth Approximation
Notes: Since order N must be an integer, value obtained is rounded up to the next highest integer.
This value of N is used to determine c by satisfying either the stopband edge (s) or the passband edge (p) specification exactly.

## Slide 25
Transfer function of an analog Butterworth lowpass filter is given by
Where,
Butterworth Polynomial:
1
1
N
1
2
3
1
1.4142136
1
1
2.0000000
2.0000000
1
4
1
2.6131259
3.4142136
2.6131259
1

## Slide 26
Example
Determine the lowest order of Butterworth LPF with a 1-dB cutoff frequency at 1kHz and minimum attenuation of 40dB at 5kHz.

## Slide 27
So we get:
The nearest integer N=4.
From the Butterworth Polynomial:

## Slide 28
Chebyshev Approximation
The magnitude-square response of an N-th order analog lowpass Type 1 Chebyshev filter is given by:
where TN() is the Chebyshev polynomial of order N:
Analog Filter Design

## Slide 29
Typical magnitude response plots of the analog lowpass Type 1 Chebyshev filter are shown below:
Chebyshev Approximation

## Slide 30
If at  = s the magnitude is equal to 1/A, then
Order N is chosen as the nearest integer greater than or equal to the above value.
Solving the above we get:
Chebyshev Approximation

## Slide 31
The magnitude-square response of an N-th order analog lowpass Type 2 Chebyshev (also called inverse Chebyshev) filter is given by:
where TN() is the Chebyshev polynomial of order N.
Chebyshev Approximation

## Slide 32
Typical magnitude response plots of the analog lowpass Type 2 Chebyshev filter are shown below:
Chebyshev Approximation

## Slide 33
The order N of the Type 2 Chebyshev filter is determined from given , s, and A using:
Example - Determine the lowest order of a Chebyshev lowpass filter with a 1-dB cutoff frequency at 1kHz and a minimum attenuation of 40 dB at 5kHz.
Chebyshev Approximation

## Slide 34
Elliptic Approximation
The square-magnitude response of an elliptic lowpass filter is given by:
where RN() is a rational function of order N satisfying RN(1/)=1/RN() ,
with the roots of its numerator lying in the interval 0<  <1 and the roots
of its denominator lying in the interval 1<  < .
Analog Filter Design

## Slide 35
Typical magnitude response plots are shown below:
Elliptic Approximation

## Slide 36
For given p, s, , and A, the filter order can be estimated using:
where
Elliptic Approximation

## Slide 37
Example
Determine the lowest order of a elliptic lowpass filter with a 1-dB cutoff frequency at 1 kHz and a minimum attenuation of 40 dB at 5 kHz.
Note: k = 0.2 and 1/k1=196.5134
Substituting these values we get:
k’=0.979796, 0=0.00255135, =0.0025513525
hence N = 2.23308
Choose N = 3.
Elliptic Approximation

## Slide 38
The Butterworth filter has the widest transition band, with a monotonically decrease gain response.
The elliptic filter has the narrowest transition band, with the equiripple passband and equiripple stopband response.
The magnitude response of the Type2 Chebyshev filter in the passband is nearly identical to that of the Butterworth.
The Butterworth and Chebyshev filters have a nearly linear phase response over about 3/4 of passband, whereas the elliptic filter has a nearly linear phase response over about 1/2 of the passband.
A Comparison of the Analog Filter Types

## Slide 39
Example: Design an analog lowpass filter of lowest order with a 1-dB cutoff frequency at 1kHz and a minimum attenuation of 40 dB at 4kHz.
[N,Wn] = buttord(Wp, Ws, Rp, Rs, 's');
[num,den] = butter(N,Wn,'s');
[N,Wn] = ellipord(Wp, Ws, Rp, Rs, ‘s’);
[num,den] = ellip(N, Rp, Rs, Wn, ‘s’);
[N,Wn] = cheb1ord(Wp, Ws, Rp, Rs, 's');
[num,den] = cheby1(N,Rp,Wp,'s');
[num,den] = cheby2(N,Rs,Ws,'s');
omega = [0: 200: 12000*pi];
h = freqs(num, den, omega);
Analog Lowpass Filter Design Using MATLAB

## Slide 40
A Comparison of the Analog Filter Types

## Slide 41
The core idea of design this kind of filter is to convert an analog transfer function Ha(s) into a digital one G(z).
There are two common methods:
(1) The impulse invariance method
(Problem9.6)
(2) The bilinear transformation method
(ch9.2)
9.2 The Design Methods of IIR Filter

## Slide 42
The Main Idea:
If a prototype causal analog transfer function Ha(s) is wanted, and its impulse response is ha(t), the impulse response of the digital transfer function G(z) satisfies:
)
(
)
(
nT
x
n
x
a
=
)
(
)
(
nT
y
n
y
a
=
)
(
]
[
nT
h
n
g
a
=
)
(
t
x
a
)
(
t
y
a
)
(
t
h
a
Supplement: The Impulse Invariance Method

## Slide 43
LT - used in continuous signal analysis
ZT - used in discrete signal analysis
Given continuous signal xa(t) , sampled signal , their LT are:
The Relationship Between ZT and LT

## Slide 44
So we can see: when , ZT=LT.
The relationship between them is a kind of mapping from s-plane to z-plane.
The ZT of the sampled sequence

## Slide 46
The mapping satisfies the essential properties ( jΩ-axis mapped onto the unit circle, stable region in s-plane mapped into the stable region in z-plane).
The relation of the normalized angular frequency w and the analog angular frequency Ω is ω= ΩT .
when Nyquist theorem is satisfied,
If is not band-limited, obtained by this method is overlapped in frequency-domain.
Discussion:

## Slide 47
The impulse invariance method design steps:
(1)Expand Ha(s) into partial-fractional:
(2)Based on , we can get:
Proof:

## Slide 48
∵From equation:
We can see the frequency response is inverse proportion of T. So we should amend it by:
(3)Usually, we scale T to , and get:

## Slide 49
The single pole sk in s-plane mapping into the single pole z=eSkT in z-plane.
They both have the same coefficients Ak .
If the analog filter is stable, that is Re[sk]<0 , then after conversion, the poles meet:|eSkT|<1, so the digital filter is stable.
The impulse invariance method only ensure relationship of the poles between s and z-plane; but for zeros, they don’t exist.
Discussion: Ha(s) and G(z)

## Slide 50: Using the impulse invariance method, we get:
If , the sampling period is T.
Then:
Example

## Slide 51: Note： is overlapped in the frequncy-domain.
When T=1，

## Slide 52
Transformation theory:
For conquering the effect of multi-value mapping from s to z-plane, we want to find a new mapping:
0
0
0
-1
1
s-plane
-plane
z-plane
9.2.1 The Bilinear Transformation
(掌握)

## Slide 53
The bilinear transformation from s to z-plane:
So, The relation between G(z) and Ha(s) is :
Note: the parameter T has no effect on the expression for G(z), and we can choose T=2 to simplify the design procedure.
The Bilinear Transformation Method
(掌握)

## Slide 54
Inverse bilinear transformation for T=2 is:
For s=σo+jΩo
Thus, σ0= 0 → |z| = 1
σ0< 0 → |z| < 1
σ0> 0 → |z| > 1
This mapping also satisfies the essential properties.
Discussion:
(掌握)

## Slide 55
For z=ej we have:
So,  = tan(/2)
This introduces a distortion in frequency axis called frequency wrapping.
(掌握)

## Slide 56
Thus, we must first prewarp the critical bandedge frequencies
and to find their analog
equivalents and by using following equation:
 = tan(/2)
(掌握)

## Slide 57
(1) Prewarp (p, s) to find their analog equivalents (p, s);
(2) Design the analog prototype filter Ha(s);
(3) Obtain the digital filter G(z) by applying bilinear
transformation to Ha(s);
Bilinear transformation preserves the magnitude response of analog filter only if piecewise constant magnitude.
Bilinear transformation does not preserve phase response of analog filter.
The Bilinear transformation design steps:
(掌握)

## Slide 58
Example – first-order lowpass Butterworth filter
Applying bilinear transformation：
9.2.2 Design of Low-Order Digital Filters

## Slide 59
where |Ha(j0)| = 0 and |Ha(j0)| = |Ha(j)| = 1
0 is called the notch frequency
If |Ha(j2)| = |Ha(j1)| = then B = 2 - 1 is the 3-dB notch bandwidth
Example - Consider the second-order analog notch transfer function:
Design of Low-Order Digital Filters

## Slide 60
Then
where

## Slide 61
Example - Design a 2nd-order digital notch filter operating at a sampling rate of 400 Hz with a notch frequency at 60 Hz, 3-dB notch bandwidth of 6 Hz
  Thus 0 = 2(60/400) = 0.3 
  Bw = 2(6/400) = 0.03 
  From the above values we get:
 = 0.90993
 = 0.587785

## Slide 62
The gain and phase responses are shown below
Thus
(掌握)

## Slide 63
将Ha(s)通过双线性变换得出
数字滤波器传输方程G(z)
将数字滤波器指标转换成模拟低通原型（analog lowpass prototype）的指标
求模拟低通原型滤波器的Ha(s)
IIR 数字滤波器设计方法
求出数字滤波器指标

## Slide 64
Consider G(z) with a maximally flat magnitude , with a passband ripple not exceeding 0.5dB; , with the minimum stopband attenuation at the stopband edge frequency is 15dB.
Base on this requirement, if we get:
9.3 Design of Lowpass IIR Digital Filters
(掌握)

## Slide 65
(1) Prewarpping:
(2) Design the prototype analog filter Ha(s)
stopband attenuation 15dB
passband ripple 0.5dB
1. The Bilinear Translation Method
(掌握)

## Slide 66
The least order of Butterworth LPF is: N=3
Using Eq.(A.8), we get the 3-dB cutoff frequency:
The third-order normalized lowpass Butterworth transfer function with c=1 is:
(掌握)

## Slide 67
(3) Design the digital filter G(z) by applying bilinear transformation
to Ha(s):
Then the denormalized lowpass Butterworth TF is:
(掌握)

## Slide 68
The third-order lowpass Butterworth transfer function which has 3-dB frequency at is:
We can get the poles and represent it as
2. The Impulse Invariance Method

## Slide 69
It is partial-fractional expressed as:
Then we get digital transfer function as:

## Slide 70
Finally,
Discussion:
Magnitude and gain responses of G(z) derived by The Impulse Invariance Method and The Bilinear Translation Method are shown below:

## Slide 72
Ex: Use a IIR digital filter to implement a Butterworth 3rd-order LPF with
sampling interval , cutoff frequency: .
① Determine normalized frequency
② Determine normalized cutoff frequency
③ Prewarping frequency to find the equivalent analog cutoff frequency
④ Choose the analog prototype filter
(掌握)

## Slide 73
Determine the transfer function of the desired digital filter using the bilinear transformation
⑥ Choose filter structure
x[n]
y[n]
1/6
-1/3
3
3
(掌握)

## Slide 74
There are two approaches as follows:
Design other type analog filters firstly, then transform it
into digital ones : Step1Step5
(2) Design digital lowpass filter firstly, then transform it into other type digital filters: Step1Step5
Please look at 9.4 to learn the detailed design procedure.
9.4 Design of Highpass, Bandpass and Bandstop IIR Digital Filters

## Slide 75
Solving: to modify the characteristics of a filter to meet the new
specifications without repeating the filter design procedure.
There are several conditions:
(1) Lowpass-to-lowpass transformation.
(2) Other transformation.
Please look at Table 9.1 to learn the detailed design procedure.
9.5 Spectral Transformations of IIR filters

## Slide 76
Order Estimation:
buttord, cheb1ord, cheb2ord, ellipord
Filter Design:
butter, cheby1, cheby2, ellip
Filter Test: freqz
Spectral Transformations:
iirlp2lp, iirlp2hp, iirlp2bp, iirlp2bs
bilinear
9.6 IIR Digital Filter Design Using MATLAB

## Slide 77
[ N, Wn ] = buttord ( Wp, Ws, Rp, Rs )
[ N, Wn ] = cheb1ord ( Wp, Ws, Rp, Rs )
[ N, Wn ] = cheb2ord ( Wp, Ws, Rp, Rs )
[ N, Wn ] = ellipord ( Wp, Ws, Rp, Rs )
[ b, a ] = butter ( N, Wn )
[ b, a ] = cheby1 ( N, Rp, Wn )
[ b, a ] = cheby2 ( N, Rs, Wn )
[ b, a ] = ellip ( N, Rp, Rs, Wn )

## Slide 78
Design of a Type 1 Chebyshev IIR digital highpass filter, Specifications:
Fp=700Hz, Fs = 500Hz,
p=1 dB, s=32dB, FT=2 kHz
Normalized angular bandedge frequencies
p =2Fp/ FT= 2700/2000=0.7
s = 2Fs/ FT= 2500/2000=0.5
Example 9.3

## Slide 79
Analog lowpass filter specifications:
p = 1, s = 1.926105 , p=1 dB, s=32 dB
Prewarping these frequencies we get
For the prototype analog lowpass filter choose p = 1
Using , we get s = 1.9626105

## Slide 80
MATLAB code fragments used for the design
[N, Wn] = cheb1ord(1, 1.9626105, 1, 32, ‘s’)
[B, A] = cheby1(N, 1, Wn, ‘s’);
[BT, AT] = lp2hp(B, A, 1.9626105);
[num, den] = bilinear(BT, AT, 0.5);
Using cheby1 design HP filter directly:
  Wp=0.7; Ws=0.5;
  Rp=1; Rs=32;
  [N,Wn] = cheb1ord(Wp, Ws, Rp, Rs);
  [b,a] = cheby1(N, Rp, Wn,‘high’);

## Slide 81
9.1, 9.2, 9.4, 9.11(a), 9.12, 9.16
M9.1, M9.2, M9.10
Homework: